## Slide 1: Efficient Computation of Flooding Scenarios for the Coast of Maine
Corinne Alini ‘18
Faculty Advisors: Laura Toma & Eileen Sylvan Johnson
Supported by the Rusack Coastal Studies Fellowship

## Slide 2
Figure 1: Destruction of Sandy
October 29, 2012
Notes: Sandy caused devastation
Why couldnt we predict sandy

## Slide 3
Predicted
Actual
Figure 2
Notes: https://project.wnyc.org/flooding-sandy-new/#12.00/40.7378/-74.0702

## Slide 4
Predicted
Actual
Notes: https://project.wnyc.org/flooding-sandy-new/#12.00/40.7378/-74.0702

## Slide 5
Figure 3: FEMA Flood Maps June 2013
Notes: Put date on this slide: New FEMA flood zones, 2013 (so that its clear that it happened after Sandy)
https://www.climate.gov/news-features/featured-images/future-flood-zones-new-york-city
Since then, noaa and coastal states have started this big effort to update their floodmaps based on slr.
The goal: extend basic flood plain to make them incorporate slr

## Slide 6: Modelling flood

## Slide 7: Surface models
Notes: To model flood, we need a model of terrain. The most commonly used model is the GRID. Basically we assume that the terrain is given to us as a grid, which represents the elevations in the terrain.
Grid models of terrain are obtained from satellite imagery, and more recently they can obtained from LiDAR technology.

## Slide 8: LiDAR data
https://aamboceanservice.blob.core.windows.net/oceanservice-prod/facts/lidar.jpg
Notes: Lidar data is very high resolution, down to 1m and below, and has great vertical accuracy (10-20 cm).
Grids obtained from LidAR data are very high resolution and basically they represent the best data available.

## Slide 9: Maine LiDAR data
Notes: LiDAR data is becoming common and Many states have at least partial coverage with high-resolution DEMs obtained from LIDAR technology.
We see all the coast has been mapped and part of inland

## Slide 10: Lincoln county, 2m resolution, 1 billion points
Notes: LT: show a picture of Lincoln county, at 2m resolution, and show how many points. Message: lidar data is large.

## Slide 12: Modeling flooding
A point is flooded if
its elevation is below the elevation of the ocean
and
the ocean can reach it (via a path of flooded points)
Algorithm idea: Simulate inundation coming from the coast. For each point on the coast, check if it is flooded. If it is, check its neighbors. Repeat.
Notes: There are two conditions that need to be met
Elevation itself isnt sufficient (lakes ex)

## Slide 13: Related work
Data: NED 10m resolution
Flooding is precomputed, users can visualize various scenarios
NOAA sea level rise viewer (https://coast.noaa.gov/slr/)
Notes: There is a body of work on modeling and viewing SLR.
For example, NOAA SLR viewer, available 2012, is using NED for the entire US at 10m res. Has precomputed flooding due to SLR on top of high tides, at various increments between 1ft and 6ft. The users can select the area that they are interested and visualize the effect of flooding. For e.g. this is the coast of Maine

## Slide 14: Related work
States are developing their own models and maps using high resolution LiDAR data, and incorporating storm flooding.
Implemented in ArcGIS
Flooding modelled via a sequence of steps
Tedious
Cannot handle large data well (use tiling)
Notes: States rely on higher resolution data and model storm flooding which noaa does not

## Slide 15: Goals
Use high resolution data (LiDAR 1-2m res)
Model slr and tides
(e.g. What will get flooded by high tide when sea rises 1 ft)
Model slr and storms
(e.g. What will get flooded by storms when sea rises 1 ft)
Outside ArcGIS, simple, efficient, open source

## Slide 16: Results

## Slide 17
DEM
(digital elevation model)
Flood zones
Flooded grid
Rise (xx ft)
Cory’s open-source, super-efficient flood model
Notes: say that you have a module that takes in the elevation model, a rise (like 3ft) and optionally a map of flood zones, and computes either:
If only a DEM and a rise are specified, computes the part of the terrain that’s flooded with that SLR
If a flood map is specified, your code essentially computes what the floodzones become with that SLR

## Slide 19: Results similar to NOAA SLR viewer
This Project
NOAA
Notes: Message: Your code gives very similar results as NOAA SLR viewer
This closeup shows it better
6ft SLR

## Slide 20: It works!
This Project
NOAA
Notes: Message: Your code gives very similar results as NOAA SLR viewer
6ft SLR

## Slide 21: It works!
Notes: Also, you spent a large part of the summer validating with the results obtained in ArcGIS by a previous Bowdoin student.
This picture shows the differences between the flooded computed by our module, and the flooding computed with the same data and same parameters, in ArcGIS by professor Eileen Johnson and her student.
We see that they are almost identical except some small patches and this big area here is due to a difference in how we interpolate, and that’s something that I am planning to fix.
We can run a 6.5GB grid, which has 1billion points in 2 minutes git st

## Slide 22
Bremen, ME
LiDAR 2m res
1ft SLR
Flooding created by this project
Notes: Here is another section of the coat, the town of Bremen. Again, Lidar data at 2m resolution. And this image shows how Bremen coast will be flooded with 1ft of SLR, as computed by our module.
(the results are very close to the results obtained in ArcGIS by prof Johnson and her previous student).

## Slide 23: Summary
Pros:
Much simpler to use than ArcGIS
Efficient (e.g. Lincoln county in under 3 minutes)
Free and open source
Versatile (combines SLR+tidal datum with SLR+storm)
Can be easily extended

## Slide 24: Thank you!
Acknowledgements
Bowdoin Rusack Coastal fellowship
Professor Eileen Johnson and Professor Laura Toma

## Slide 25: References
Pictures, Michael Shaw Reading The. "Sandy: Sin City." Reading The Pictures. October 29, 2012. Accessed July 20, 2017. http://www.readingthepictures.org/2012/10/sandy-2-a-threat-to-our-very-way-of-life/; Soliwon, Diana. "20 Then-and-Now Photos of Hurricane Sandy." U.S. News. October 29, 2013. https://www.usnews.com/news/articles/2013/10/29/photos-hurricane-sandy-then-and-now.;Emergency Blog. Accessed July 20, 2017. https://emergencyblog.americares.org/2012/12/helping-staten-island-communities-recover/dsc_0698/.
"Flooding and Flood Zones | WNYC." Project.wnyc.org. Accessed July 20, 2017. https://project.wnyc.org/flooding-sandy-new/#12.00/40.7378/-74.0702.
Future Flood Zones for New York City | NOAA Climate.gov. March 18, 2014. Accessed July 20, 2017. https://www.climate.gov/news-features/featured-images/future-flood-zones-new-york-city.
"Flood Maps And Flood Zones." Flood Elevation Surveyors. Accessed July 20, 2017. http://floodelevationsurveyors.com/flood-zones.html.
US Department of Commerce, National Oceanic and Atmospheric Administration. "What is LIDAR." NOAA's National Ocean Service. October 01, 2012. Accessed July 20, 2017. https://oceanservice.noaa.gov/facts/lidar.html.

## Slide 26
Figure 4: BFE
Notes: Ref: http://www.riskmap3.com/node/998